## Slide 1
RISC-V K1 | VLEN=256 | RVV + IME | OpenMP
Heterogeneous RVV-IME GEMM
OpenMP is used to schedule C tiles across K1 cores; RVV and IME kernels do the arithmetic.
01
HETEROGENEOUS_RVV_IME_OPENMP_GEMM
Objective
Measure how existing GEMM micro-kernels behave when they run together across the full K1 board.
Input
Existing RVV and IME micro-kernels.
OpenMP layer
Creates worker threads and gives each worker C-column tiles.
Output
Time, GFLOPS/GOPS, CPU placement, and tile counts.
GEMM equation stays unchanged: C(i,j) = C(i,j) + sum_k A(i,k) x B(k,j)

## Slide 2
RISC-V K1 | VLEN=256 | RVV + IME | OpenMP
K1 Mapping and C-Tile Split
The output matrix C is divided by columns because each column tile is an independent output region.
02
HETEROGENEOUS_RVV_IME_OPENMP_GEMM
K1 cores 0-3
IME-capable domain.
K1 cores 4-7
RVV domain.
Thread placement
taskset + OMP_PLACES=cores + OMP_PROC_BIND=close.
For N = 1024 and tile_N = 32
C-column tiles = 1024 / 32 = 32
A and B are shared reads. C is split into separate write regions.

## Slide 3
RISC-V K1 | VLEN=256 | RVV + IME | OpenMP
OpenMP Library Role
OpenMP manages threads and safe tile ownership; the RVV/IME kernels remain the compute engines.
03
HETEROGENEOUS_RVV_IME_OPENMP_GEMM
Compile
-fopenmp links the OpenMP runtime.
Create workers
#pragma omp parallel starts the worker team.
Control workers
OMP_NUM_THREADS selects the number of workers.
Bind to cores
taskset, OMP_PLACES=cores, and OMP_PROC_BIND=close guide placement.
Claim tiles
#pragma omp atomic capture protects next_tile.
Call kernels
call_tile_kernel(...) selects RVV, IME, or mixed mode.
#pragma omp parallel -> sched_getcpu() -> atomic tile claim -> call_tile_kernel(...)

## Slide 4
RISC-V K1 | VLEN=256 | RVV + IME | OpenMP
Scheduler Algorithm
The scheduler is the main OpenMP tiling logic.
04
HETEROGENEOUS_RVV_IME_OPENMP_GEMM
start worker
read CPU
take next C tile
dispatch kernel
record result
Key source file
src/openmp_tile_scheduler.h
This file contains the OpenMP tile loop, CPU detection, tile claiming, and worker tile counters.
Meaning: every worker owns a C tile before it calls the RVV or IME kernel.

## Slide 5
RISC-V K1 | VLEN=256 | RVV + IME | OpenMP
Source Roadmap
The implementation is small enough to explain with five files.
05
HETEROGENEOUS_RVV_IME_OPENMP_GEMM
01
src/openmp_heterogeneous_gemm.c
Benchmark entry point: parses setup, starts timing, prints CSV results.
02
src/openmp_tile_scheduler.h
OpenMP tiling: splits C, claims tiles, records worker CPUs and tile counts.
03
src/openmp_kernel_dispatch.h
Kernel dispatch: selects the RVV, IME, or mixed execution path.
04
src/openmp_validation.h
Validation: compares computed output when checking is enabled.
05
scripts/run_openmp_tiled_gemm_mode.sh
Run script: builds with -fopenmp and sets CPU/OpenMP variables.
Main file to show for OpenMP scheduling: src/openmp_tile_scheduler.h

## Slide 6
RISC-V K1 | VLEN=256 | RVV + IME | OpenMP
Comparison Evidence
The same performance metrics are used for single-core and OpenMP runs.
06
HETEROGENEOUS_RVV_IME_OPENMP_GEMM
Core-isolated
One kernel on one pinned core.
OpenMP domain
RVV-only or IME-only tiles across selected cores.
Mixed RVV-IME
Both domains cooperate on the same GEMM.
Result files
k1_01_rvv_ime_summary_latest.csv | openmp_summary_latest_k1-rvv.csv | openmp_summary_latest_k1-ime.csv | k1_openmp_heterogeneous_summary_latest.csv
Metrics: time_sec, GFLOPS, GOPS, mean, median, standard deviation.
Final message: single-core tests measure kernels; OpenMP tests full-board execution.