## Slide 1
RISC-V K1 | INT8 GEMM | VLEN = 256 bits
Accuracy Equivalence of IME and RVV GEMM
How we prove that the IME and RVV integer kernels produce the same matrix answer
WHAT MUST BE TRUE
IME answer = RVV answer = trusted answer
Trusted answer means the same matrix multiplication computed independently with larger INT64 numbers.
All 1,048,576 output values must match exactly; one wrong value means the test fails.
Methodological basis: Ozaki, Uchino, and Imamura, Ozaki Scheme II, arXiv:2504.08009.

## Slide 2
METHOD
How the Ozaki Idea Guides This Test
The paper motivates low-precision GEMM error measurement; our experiment applies that reasoning to two integer kernels.
02
WHAT OZAKI DOES
Build accuracy from small parts
Split floating-point matrices into lower-precision parts, multiply those parts, and combine the partial answers.
With s matrix slices:
low-precision GEMMs = s(s + 1) / 2
WHAT THIS STUDY DOES
Compare two kernel answers
Give IME and RVV the same INT8 matrices, then compare both INT32 answers with one independently calculated INT64 answer.
For an M x N x K matrix product:
multiply-adds = M x N x K
Taken from Ozaki: compare against a trusted answer and report the largest numerical difference.
Different from Ozaki: we do not emulate floating point or use CRT; we test whether IME and RVV perform the same INT8-to-INT32 math.
Source: Ozaki et al., arXiv:2504.08009, Sec. 2.2 and Fig. 1; adaptation boundary stated explicitly for reproducibility.

## Slide 3
NUMERICAL SAFETY
Can INT32 Hold the Largest Possible Answer?
We multiply the largest possible INT8 values and add 1,024 products.
03
128
largest size of one signed INT8 input
16,384
largest product: 128 x 128
1,024
products added for one output value
16,777,216
largest possible final output size
largest answer <= K x largest A value x largest B value
= 1,024 x 128 x 128 = 16,777,216 = 2^24
INT32 positive limit = 2^31 - 1 = 2,147,483,647
INT32 is about 128 times larger than the worst-case answer, so overflow should be zero.
This is a worst-case calculation: actual random inputs normally produce smaller sums.

## Slide 4
MATRIX MULTIPLICATION
How One Output Number Is Made
Take one row from A and one column from B, multiply matching values, and add the products.
04
ROW i FROM MATRIX A
[ 2 -1 3 ]
three values from one row
x
COLUMN j FROM MATRIX B
[ 4 5 -2 ]
three matching values
=
ONE OUTPUT: C(i,j)
2 x 4 + (-1) x 5 + 3 x (-2)
= 8 - 5 - 6 = -3
multiply first, then add
For the real 1024 x 1024 x 1024 experiment:
one output = 1,024 products added together
number of outputs = M x N = 1,048,576
total multiply-adds = M x N x K = 1,073,741,824
The trusted INT64 calculation and both optimized kernels must produce the same C(i,j) value at every row and column.

## Slide 5
VALIDATION ALGORITHM
How Every Output Value Is Checked
The trusted answer is calculated separately from both optimized kernels.
05
Create A and B
same random INT8 input values
Trusted answer
normal row-by-column math using INT64
Kernel answer
run IME or RVV using INT32 output
Compare answers
check all 1,048,576 output values
Save results
CSV summary and difference histogram
Difference for one output position (row i, column j)
difference(i,j) = abs(kernel answer(i,j) - trusted answer(i,j))
Largest difference
largest = max(difference)
Wrong output values
wrong = count(difference > 0)
Correct percentage
correct = (MN - wrong)/MN x 100
PASS only when: largest difference = 0, wrong outputs = 0, correct = 100%, overflow = 0
The C checker performs this comparison independently for the IME-native and RVV-fallback paths.

## Slide 6
MEASURED EVIDENCE
Full-Range INT8 Results on K1 (1024 x 1024 x 1024)
Real CSV values for VLEN=256 bits; each row combines the tested kernel settings.
06
Kernel path
Output block
Vector grouping
Correct runs
Success
Most wrong outputs
Largest difference
IME native
8x4
LMUL 1
16 / 16
100%
0
0
RVV fallback
8x4
LMUL 1 + 1/2
8 / 8
100%
0
0
IME native
8x4
LMUL 1/2
0 / 16
0%
1,048,571
1,402,086
IME native
8x8
LMUL 1 + 1/2
0 / 32
0%
1,048,576
1,470,339
RVV fallback
8x8
LMUL 1 + 1/2
0 / 8
0%
1,048,574
1,255,732
The archived data confirms the 8x4 IME LMUL1 and 8x4 RVV paths. The other listed variants failed this exact test.
Vector grouping is the plain-English meaning of LMUL. Data source: full_range_uniform, ZVL=256b, campaign 2026-06-09.

## Slide 7
CONCLUSION
When Are IME and RVV Mathematically Equal?
They are equal only when both match the same independently calculated answer.
07
Simple equality rule
IME answer = trusted answer, and RVV answer = trusted answer => IME answer = RVV answer
The mathematical check
abs(IME - RVV)
<= abs(IME - trusted) + abs(RVV - trusted)
= 0 + 0 = 0
How to report the result
1. Say equal only when every output value is correct.
2. Show failed kernel settings instead of hiding them.
3. Repeat this test whenever the kernel code changes.
Conference message
The contribution is a repeatable test that proves which RISC-V IME and RVV integer kernels calculate exactly the same matrix.
Reference: K. Ozaki, Y. Uchino, and T. Imamura, Ozaki Scheme II, arXiv:2504.08009 (2025).